## Slide 1: Structured appRoach to geotechnical logging
for Mining and Civil Applications
Carel de Beer
Senior Geotechnical Consultant
Sound Mining Solution

## Slide 2: Why do we log core?
“Because the senior geologist said so”
“I don’t know”

## Slide 3: Why do we log core?
To determine rock mass parameters for mine or foundation design
To get as much relevant information from the core as possible

## Slide 4: Systems in Use
Civil
  DOTPLOT
  Excel
Mining
  Excel
  Aquarius
  SABLE
  ect.
No UNIVERSAL STANDARD in SA

## Slide 5: Quality Drilling Program
Define clear expected outcomes
Choose the correct drilling method and size
Use a experienced drilling contractor
Good drilling management
Use an experienced engineering geologist/technologist
Define the logging standard to be used
Log the core at the drill rig

## Slide 6: Quality Logging
Log core on a daily basis at the rig
Process:
  Material Recovery Log per core run (incl. RQD)
  Geotechnical Unit (Rock material description)
  Discontinuity Description per set
  Sample selection
  Point Load Testing
  Core Photograph

## Slide 7: Rock Mass Description
Rock Material
  Moisture
  Colour
  Fabric
  Texture
  Rock mass strength
  Weathering/decomposition
  Fracturing
  Rock type

## Slide 8: Rock Mass Description
Discontinuity description per set
  Type
  Spacing
  Orientation
  Persistence
  Roughness
  Waviness
  Wall separation
  Fill thickness
  Infill type
  Fill strength
  Wall strength
  Wall weathering

## Slide 9: Complete Rockmass Description
Only 20 parameters (8Rock 12 discont.)
Each parameter has a predefined list of options
  ROCKMASS STRENGTH
    Very weak (1 – 3 MPa)
    Weak (5- 10 MPa)
    Medium strong (10-25 MPa)
    Strong (25-50 MPa)
    very Strong (50-150 MPa)
    Extremely Strong (150+ MPa)

## Slide 10: Data Mangement
Relational Database for material recovery, rock-mass description, point-load tests, de-survey log, acoustic log and lab results.

## Slide 11: Example of Logsheet

## Slide 12: Important
Conduct drilling management. Driller has up to 20% influence on your final rock mass rating.
Proper geotechnical drilling is expensive. Get as much information from that core you can. Now.
Don’t log for a specific rock mass classification system!
Do a complete description (20 parameters)

## Slide 13: Questions ?